## Slide 1: Complex network geometry and navigation
Dmitri Krioukov CAIDA/UCSD F. Papadopoulos, M. Kitsak, kc claffy, A. Vahdat M. Á. Serrano, M. Boguñá UCSD, December 2010

## Slide 2
Notes: In maze without the MAP
Learning its MAP
Dynamic
More complex

## Slide 3
Notes: Direction would be good
Efficiency
Optimality
Robustness
Geometry!!! (no geometry on the previous slide!)
BEST POSSIBLE if all these conditions satisfied

## Slide 4
Notes: Nodes are intersections, links are maze sections between intersections
Complex network: hubs and clustering (not all intersections have just 3-4 roads coming in)
Many real networks are like that
Navigation in real networks
  Internet
  Brain
  Regulatory
  Milgram
No global knowledge
Except in the Internet
  Routers
  Distributed topology learning
  Shortest path computations
  Topology changes, update, recomputations
  Black holes
  Major scalability problem
  It would be great to route in the direction
  To have a direction we need a geometric map

## Slide 5
Notes: No node has any global knowledge
Congruency is needed (for efficiency, optimality, and robustness)
If congruency is there, shortest paths in network are discrete reflections of smooth shortest (geodesic) paths in the space

## Slide 6
Notes: Exactly the picture from the previous slide
Blue disc = grey surface
Blue disc is HYPERBOLIC

## Slide 7
Notes: Exponential expansion
Geodesics are not straight lines

## Slide 8
Notes: How constructed
Why nodes are not connected at the periphery

## Slide 35: Navigation efficiency and robustness (synthetic networks)
Percentage of successful greedy paths 99.99%
Percentage of shortest greedy paths 100%
Percentage of successful greedy paths after removal of x% of links or nodes
  x10%  99%
  x30%  95%

## Slide 36: Success ratio in random graphs
Configuration model (the same degree distribution) 30%
Classical random graphs (the same average degree) 0.17%

## Slide 37: Mapping the real Internet using statistical inference methods
Measure the Internet topology properties
Map them to model parameters
Place nodes at random hyperbolic coordinates
Apply the Metropolis-Hastings algorithm to find the coordinates maximizing the likelihood that Internet is produced by the model

## Slide 40: Navigation efficiency and robustness (Internet)
Percentage of successful greedy paths 97%
Average stretch 1.1
Percentage of successful greedy paths after removal of x% of links or nodes:

## Slide 41
Why?
  Congruency between hyperbolic space geometry and scale-free network topology
  Hierarchical/heterogeneous organization of the two (zooming-out/zooming-in pattern)
  Strong clustering/metric structure
How?
  Strong clustering yields high path diversity
  All paths are congruent to their corresponding hyperbolic geodesics
  If some paths are damaged, many others remain, and can still be found since they all congruent

## Slide 42
No routing information exchange upon topology changes
  if the minor degradation of routing efficiency is tolerable
Slightly more intelligent variations of greedy forwarding, using small amount of non-local information, sustain 100% routing efficiency

## Slide 43: Take-home message


?

## Slide 44: Open question
Does any optimization of efficiency and robustness of targeted transport drive network evolution explicitly?
Or is it just a natural but implicit by-product of other (standard) network evolution mechanisms?

## Slide 45: Summary (of other results)
We have discovered a new geometric framework to study the structure and function of complex networks
The framework provides a natural (no “enforcement” on our side) explanation of two basic structural properties of complex networks (scale-free degree distribution and strong clustering) as consequences of underlying hyperbolic geometry
The framework admits a standard statistical physics approach (exponential random graphs), interpreting auxiliary fields as linear function of hyperbolic distances/energies
The framework subsumes the configuration model, classical random graphs, and random geometric graphs as three limiting cases with degenerate geometric structures
The framework explains how the hierarchical structure of complex networks ensures the maximum efficiency of their navigation function – optimal routing without global topology knowledge
The framework provides a basis for mapping real complex networks to their hidden/underlying hyperbolic spaces

## Slide 46: Applications of network mapping
Internet
  optimal (maximally efficient/most scalable) routing
  routing table sizes, stretch, and communication overhead approach their theoretical lower bounds
Other networks
  discover hidden distances between nodes (e.g., similarity distances between people in social networks)
    “soft” communities become areas in the underlying space with higher node densities
  tell what drives signaling in networks, and what network perturbations drive it to failures (e.g., in the brain, regulatory, or metabolic networks)

## Slide 47
M. Boguñá, F. Papadopoulos, and D. Krioukov, Sustaining the Internet with Hyperbolic Mapping, Nature Communications, v.1, 62, 2010
D. Krioukov, F. Papadopoulos, A. Vahdat, and M. Boguñá, Hyperbolic Geometry of Complex Networks, Physical Review E, v.82, 036106, 2010, Physical Review E, v.80, 035101(R), 2009
F. Papadopoulos, D. Krioukov, M. Boguñá, and A. Vahdat, Greedy Forwarding in (Dynamic) Scale-Free Networks Embedded in Hyperbolic Metric Spaces, INFOCOM 2010, SIGMETRICS MAMA 2009
M. Boguñá, D. Krioukov, and kc claffy, Navigability of Complex Networks, Nature Physics, v.5, p.74-80, 2009