## Slide 1: Measured Impact of Crooked Traceroute
Matthew Luckie, David Murrell (Univ. of Waikato)
Amogh Dhamdhere, kc Claffy (CAIDA/UCSD)

## Slide 2: The Problem
Traceroute-based algorithms are critical to macroscopic topology collection efforts
Until recently, such algorithms ignored the effects of per-flow load balancing
Classic traceroute + per-flow load balancing:
  Inference of false loops -- Augustin et al. IMC ’06
  Lower destination reachability -- Luckie et al. IMC ’08
  Inference of false links

## Slide 3: The Problem
Classic traceroute: probes toward a destination can take different paths
  Augustin et al. IMC’07: 39% of paths have at least one per-flow load-balancer
We try to quantify false link inference rate
Can’t go back and fix pre-2006 data
X
B
Y
A
D
C
0
1
0
2
0
0
0
1
1
0
1
1
1
2
X0
A0
D0
Y0
X0
B0
C0
Y0

## Slide 4: Terminology
Artifact links: links that are inferred by classic traceroute but not actually traversed by packets in ﬂows
Artifact links would not be inferred with a traceroute algorithm that enumerates per-ﬂow load-balanced paths toward the destination, e.g., MDA traceroute
An artifact link is not necessarily false!
False links: Artifact links which we believe to not exist in the topology

## Slide 5
X
Y
A
B
C
D
E
F
Interface graph
With load balancing at X, A, and B, MDA traceroute would see this graph

## Slide 6
X
Y
A
E
Interface graph
Inferred using classic traceroute
B
C
D
F
A-E is an artifact of classic traceroute

## Slide 7
X
Y
A
E
B
C
D
F
A-E does not introduce a false link if A+B are aliases in the router topology
Interface graph
revealed using classic traceroute
X
A,B
Y
C
D
E
F

## Slide 8
X
Y
A
E
B
C
D
F
A-E does not introduce a false link if C+E are aliases in the router topology
Interface graph
revealed using classic traceroute
X
C,E
Y
D,F
A
B

## Slide 9
X
Y
A
E
B
C
D
F
A-E could introduce a false link in this router topology
Interface graph
revealed using classic traceroute
X
C,D
Y
E,F
A
B

## Slide 10: Not all load balancing could produce an artifact
X
Y
A
B
C
D
E
F
X
C
A
B
Y
D
X
Y
A
B




## Slide 11: Methodology
22 ark monitors, each probing a list of 16189 addresses
  Derived from BGP data from Routeviews in Sept 2010
Identify artifact links in classic traceroute data
  MDA to infer all possible links towards a destination to 99% confidence
  Artifact links appear in the output of classic traceroute but not in MDA traceroute
Determine if the artifact could introduce a false router link

## Slide 12: Identifying False Links
A
E
B
C
D
F
Use Ally and Mercator to check for aliases
If (A,B) or (E,C) or (E,D) are aliases, then the artifact link is not false (classification: valid)
If (A, B, C, D, E) all exhibit incrementing IPID but no alias is found, the artifact could be a false link
Otherwise artifact is unclassified.
Assumption (validated) is that IPID-based alias resolution can determine whether or not two IP addresses are aliases if incrementing IPID values are observed.

## Slide 13: Routing Changes
To guard against false positives as a result of path changes, we use the following procedure
  Initial Paris traceroute
  Classic traceroute
  MDA traceroute to 99% confidence
  Final Paris traceroute
Infer stable routing if neither Paris trace infers a link not also seen with MDA

## Slide 14: Summary of Results
Total IP-level links | ICMP | UDP
Classic | 427,211 | 413,040
Paris | 422,130 | 398,179
MDA | 455,965 | 462,762
Artifact links | 13,313 | 32,233
Fraction of classic links | 3.12% | 7.8%
Inferred valid | 45.9% | 38.6%
Inferred false | 24.3% | 34.7%
Unclassified | 29.9% | 26.7%
False Links | 3,230 | 11,179
Fraction of classic links | 0.76% | 2.71%

## Slide 15: False AS links
Traceroute is often used to infer AS-level connectivity
  Using prefix-AS mapping on each interface
False router links in classic traceroute can cause false AS links
26733 AS links in UDP-based graph, 28591 in ICMP graph
58 false AS links in UDP, 23 in ICMP
3 AS links (UDP) and 2 AS links (ICMP) were found in UCLA’s BGP AS topology

## Slide 16: ISP-level Impact of False Links
We found small impact of false links on macroscopic topology
But what about mapping specific ISPs?
Obtained ground truth from tier-1 ISP: 1986 routers, and set of interfaces on each router
Probed prefixes in ISP’s customer cone from 265 Planetlab sites
Observed interfaces from ~45% of ISP’s routers, ~1400 links with Paris traceroute, ~4000 with Classic

## Slide 17: ISP Router Degree Distribution
UDP-Classic makes the ISP appear to have much richer connectivity
Router degrees inflated by a median factor of 2.9 in UDP-Classic vs UDP-Paris

## Slide 18: ISP PoP-level Path Diversity
We map routers to PoPs using geographic information
We compute the number of edge and node-disjoint paths between each pair of PoPs
UDP-Classic overestimates path diversity

## Slide 19: Summary
Quantified the impact of classic traceroute + per-flow load balancing
Macroscopic topology: small impact
  0.76% of links in classic ICMP traceroute are invalid
  2.71% of links in classic UDP traceroute are invalid
Classic ICMP-echo approach not as affected by per-flow load balancers as UDP
ISP mapping: larger impact
  Classic traceroute overestimates router degrees (median factor 2.9), PoP level path diversity

## Slide 20: Thanks! Questions?
www.caida.org/~amogh/crooked-CCR10.pdf

## Slide 21: Artifact link impact: analytical alias resolution
Analytical alias resolution rule: two addresses in a traceroute path can’t be aliases if there are no loops.
X
C
A
B
Y
D
0
0
0
0
1
0
0
X
C
Y
1
Y
D
0
0
0
0
10-15% of false links are of this form

## Slide 22: Validating use of Ally technique to classify artifact links
Use ping –R and ICMP-Paris traceroute towards destination
  RR IP address usually from egress interface
  ICMP time-exceeded IP address usually from ingress interface
Infer addresses used in a sequence of /30 subnets
Identify ICMP/TCP/UDP IP-ID behaviour for each
Resolve for aliases using Ally for pairs of addresses with incrementing IPID values.
a.b.c.5
a.b.c.6
d.e.f.86
d.e.f.85
g.h.i.194
g.h.i.193
traceroute
RR

## Slide 23: Validating use of Ally technique: results
22 ark monitors, 26,510 pairs of likely /30 aliases tested
Classification obtained for 20,762 (78%)
  Others did not have an incrementing IP-ID
  Some were incrementing but unresponsive to Ally.
93.8% inferred as aliases
  Of not aliases, 6 IPs are involved in 88% of pairs
  Suggests 6 outliers rather than a systematic erro