## Slide 1: Measuring Mobile Broadband Availability in Norway
Ahmed Elmokashfi and Amund Kvalbein

## Slide 2
Over 100 measurement points in
10 municipalities
Measure the availability
and quality of multiple
operators

## Slide 3
Each measurement node is multihomed to four ISPs
ICE
NetCom
  Fixed
Brønnøysund
Simula
Internet
Telenor
For more information: http://nevada.simula.no/

## Slide 5
We measure the gaps in monitors ping time series
203 interfaces
- 64 fixed, 56 ICE, 54 Telenor, 29 Netcom
Three months duration (May ‘11-July ‘11)
Downtime
Is a downtime if g>=15 seconds
g

## Slide 6
There are large differences in stability between operators and between monitors in the same operator
10 minutes per day

## Slide 7
Major failure events have only a slight impact on the measured downtime

## Slide 8
Most outages are short-lived lasting less than 3 minutes
CCDF
Failure Duration(Seconds)

## Slide 9
Failures tend to be clustered. About 70% of all failures are spaced by less than 100 seconds
Up time (Seconds)
CCDF

## Slide 10
Monitors do not fail independently
Telenor
ICE

## Slide 11
Failures affecting multiple monitors simultaneously contribute significantly to the overall downtime

## Slide 12
In ICE, geographically close monitors are more likely to fail simultaneously
Telenor
ICE
An ICE base station covers a larger geographical area

## Slide 13
Combining all three MBB operators increases the overall availability to 99.98%
Telenor | Netcom | ICE
99.51% | 99.83% | 99.73%
2 minutes
18 seconds

## Slide 14
What’s next?
New measurement nodes
External data sources
Mobile Apps